SC22 Replace Me With Real Template

---
hard
Software and Hardware: A strained relationship
- Hardware gets designed by hardware guys, software gets designed by software guys
- Hardware has constraints: feature size, power draw, heat dissipation, complexity
- Systems software has constraints, too: hardware and its capabilities
- But we use hardware to actually do computing work. So as workloads and software changes, hardware has to and does change.
- But only slowly: VMWare released in 1999, vt-d/amd-v come in 05/06.
- ~6 year lagtime!
Intel VT-D
VMWare released
AMD-V
1999
2000
2001
2002
2003
2004
2005
2006
2007
2008
2009
2010

---
Why is it like this? What can we do?
- Chips are very hard to make. Circuit design, simulations, tapeouts, fabrication delays, costs, etc.
- Companies are reluctant to “just try stuff”
- Hardware features may not get used anyway: hardware task-switching, x86’s rings 1 and 2, etc.
- The components of co-design:
  - Reduce time/cost to prototype hardware: FPGAs
  - Reduce difficulty to extend ISAs: RISC-V
  - Reduce difficulty to test new hardware: extensible, simple software

---
Extensible, simple software: this work
- The grand vision is to do co-design, mainly in HPC and confidential/secure computing
- We need a suitable kernel to test this (possibly very experimental) hardware
  - This work is a stepping stone toward that vision
- So, to start, we port Kitten

---
Co-Design is as hard as you make it: complexity
- The “semantic gap” is a design barrier between hardware and software that allows increased complexity
- But, at the cost of decreased complexity
  - Hardware assumes software wants some features, like MMUs, cache coherence, etc.
  - Software assumes hardware provides some features, and designs mechanism that exploit those features: paging, processes, multi-processing
- The difficulty only arises when both sides are complex:
Design decisions
?
Design decisions
Design decisions
HW
SW
HW
SW
HW
SW

---
What kind of hardware complexity do we want?
- An open-source ISA is critical to co-design.
  - Try asking Intel, AMD, etc. to try an experimental change
  - Xtensa controllers are an option, but not targeted at research/academia
- RISC-V has a good supply of research hardware implementations, exploring a wide variety of architectural ideas (just a few examples):
  - Pipelining: SHAKTI
  - Superscalar: Berkeley’s RISC-V BOOM
  - VLIW: Packet Manipulator
  - Manycores: Hammerblade, Manticore

---
What kind of software complexity do we want?
- The obvious choice? Linux!
  - However, Linux’s enormous complexity makes modification hard, to say the least.
  - The task struct on Linux is ~800 lines long:

---
What kind of software complexity do we want?
- Kitten is a simple, capable kernel that uses fewer hardware abstractions than Linux and uses simpler ones whenever possible.
- Kitten is optimized for performance in HPC contexts and can provide Linux ABI compatibility.
  - Larger memory page sizes by default
  - Contiguous, linear memory mapping
  - Simple, round-robin task scheduling
- And we already ported it to ARM64

---
Objectives of the Port
- ✅ Platforms: QEMU, SiFive Unmatched
- ✅ Benchmarks: HPCG, STREAM, RandomAccess
- OS Features:
  - ✅ Single-process support
  - ✅ FPU
  - ✅ Timers
  - × Interrupts
  - × Multi-process
  - × Multi-core
- But these are on the way!

---
Some interesting lessons learned
- Some interesting challenges faced along the way:
  - Paging structure
  - Linker relaxations
  - Register quantity vs ARM and thread-local storage
  - L2 cache or scratchpad memory
  - L2 cache prefetchers and performance

---
Paging Structure
- Borrow heavily from Linux when possible, can’t borrow here.
  Write from scratch.
- RISC-V paging structure is very simple. Pick a bit-width (39-bits here) and here’s your format. From the Unmatched manual:

---
Paging, continued
- Leafs are found by checking the RWX permission bits
- Accessed/Dirty are controlled by the kernel, not the hardware
  - Though an exception will be generated if they are wrong!
- A toggle to cause a fault on OS read/write to user pages.
  - An interesting opportunity for kernel-managed, secure pages?
- Less C structs to manage, simpler memory code

---
Linker relaxations
- RISC-V is a register-rich, but addressing mode-poor ISA.
- Addressing any 32-bit address requires two instructions:
  - lui/auipc to set hi-20 bits
  - ld to specify lo-12 bits
- But RISC-V provides a global pointer (gp), which typically points to a part of the BSS section, the small BSS (.sbss).
  - Kitten has to load this to the right place
  - Have to juggle it when switching from physical to virtual memory, too
- The global pointer allows us to elide the auipc/lui instruction
- There are other registers, too, that could be extra gps.
  - Would allow for more relaxation and thus faster access
  - Require toolchain support, like GCC on ARM64 preserving an extra register for system use

---
Register Quantity and Thread-Local Storage
- RISC-V has a good supply of general-purpose registers, but comparatively few system registers.
  - When switching tasks, need to store kernel stack, task struct pointer, etc.
  - ARM64 has “banked registers” containing context at each level: stack pointer, thread pointer
- RISC-V has one architectural “scratch” register per level
  - So what do we do? We emulate Linux: put the thread info struct at offset 0 inside the task struct, and point tp to both of them
  - Fetch the kernel stack from there

---
SiFive Unmatched and L2 Cache
- The SiFive Unmatched has a very flexible L2 cache that can serve as L2 cache, scratchpad, direct memory, or some mix of all three.
- At boot time, must enable cache ways.
- Enabled ways can be written to as a scratchpad (where evictions might occur at any time)
- Disabled ways can be directly addressed and used as ordinary RAM
  - Interesting opportunities for accelerated locks, message-passing buffers, etc.

---
Performance and cache prefetchers
- To assess port completeness and correctness as well as characterize hardware, we ran typical benchmarks on QEMU and the Unmatched
- The Unmatched lacks an L2 prefetcher.
  - This has some consequences for memory performance.

---
Performance: HPCG
- HPCG: A typical benchmark, a decent mix of memory and compute intensiveness.
- Kitten on QEMU on the workstation outperforms the Unmatched by a factor of about 2.

---
Memory Performance: STREAM and RandomAccess
- Two common benchmarks to characterize memory performance
- QEMU shows a substantial advantage in STREAM, but not in RandomAccess.

---
RandomAccess

---
Thank you!
Feel free to ask any questions you have.